RISC-V for AI
Progress

---
Week 5:
Agenda:
1. Compiler Optimization
2. Execution on Raspberry Pi3
3. Profiling Results for Convolution, Maxpooling and Matrix-Vector Multiplication operations

---
Compiler Optimization
- Usage of gcc flag: -O3
- Results in (1/4) execution time and (1/8) code size
- The Assembly Code reveals the usage of SIMD Instructions in x86 and NEON-Vector Extension Insturctions in ARM
https://www.rapidtables.com/code/linux/gcc/gcc-o.html

---
Intel Corei3 8145U CPU Specs.
No. of Cores	64-bit Dual -core/Two computing threads per core
CPU Clock Speed	2.1 Ghz to 3.9 GHz
Memory	12 GB DDR4
Cache Organization	L1: 128 KiB ->L1i = 64 KiB , L1d = 64 KiB, 8 -way Set Associative / L2: 512 KiB ->4 Way Set Associative / L3: 4 MiB -> 12 Way Set Associative
ISA Extensions	Supports SIMD, Vector Extensions
https://en.wikichip.org/wiki/intel/core_i3/i3-8145u

---
ARM Cortex A53 (BCM2837 SoC)
CPU	4 x ARM Cortex A-53, 1.2 GHz
RAM	1GB LPDDR2
Cortex A53 Processor	2-wire decode superscalar, 8-stage pipelined , in-order execution (based on ARM v8-A ISA)
ISA Extension Support	Floating Point, DSP, NEON SIMD Instructions
Cache	64-byte lines / L1 -8KiB to 64 KiB / L2 – 128 KiB to 2MiB

---
Comparison of Execution Times
Function	x86	Cortex A53	x86 with 03	A53 with O3
CNN_main()	228 205 668	227 123 968	59 625 565	59 916 093
Conv2d_2() / Image =[12 , 12] / kernel = [5,5,32,64]	201 948 748	196 015 915	57 662 471	57 727 822
Conv2d_1() / Image = [28, 28] / Kernel = [5,5,1,32]	24 691 568	29 450 033	1 703 225	1 833 513
Maxpool2_1() / Inp = [24,24]	638 077	671 422	109 532	128 582
Perceptron(2-layer) / 1024 -->10	391 168	411 898	125 477	197 073
relu	10	14	2	5.5
Maxpool2_2 / Inp = [8,8]	101 441	173 322	24 474	28 728
max4	21	18	4	10

---
Profiling Analysis for CNN
Analysis of Innermost Loop of Convolution
{
        filt_offset = x*((FILT1_DIM2)*(FILT1_DIM3)*(FILT1_DIM4))\
        + y*((FILT1_DIM3)*(FILT1_DIM4))\
        + z*(FILT1_DIM4)\
        + output_depth;
        img_offset = (output_row+x)*((IMG_DIM2)*(IMG_DIM3))\
        + (output_col+y)*(IMG_DIM3)\
        + z;
        sum+= filter[filt_offset] * img[img_offset];
        }
No. of Iterations : 3 276 800

---
Inner Loop Analysis contd...
No. of Iterations : 3 276 800
Parameter	x86	Cortex-A53	X86 with O3	A53 with O3
No. of instructions	54	50	7	7
CPI	1 for all except / 11.10 for 1 movss	1 for all except / 11.097 for 1 vld	1 for all except / 11.10 for 1 movss	1 for all except / 11.097 for 1 vld
Observations:
1. For computing the Matrix offsets, both x86 and ARM compilers have
    replaced all multiplications with a combination of SLL and ADD
2. All Loads appear to take 1 clock cycle for L1- Cache hit.
3. Instruction distribution: LD (13), ADD(12), LSL(8), STR(4), MOV
4. Possibility of Improvement: Even with -O3 optimization, the loop executes for 3276800 times.
    Possibly imptrove by unrolling the inner loop 5 x 5 x 32 (800 - 1) times by accepting image and filters as vectors.
5. -O3 uses instructions such as vmla (mac) , vpust/pop (multiple regs to mem), vldmia(load multiple)

---
Profiling Analysis for Maxpool Operation
   for (int row=0; row<MAXPOOL2_DIM1;row++)
    {
        for (int col=0;col<MAXPOOL2_DIM2;col++)
        {
        for (int depth=0; depth<MAXPOOL2_DIM3;depth++)
        {
        e1 = row*2*(CONV2_DIM2)*(CONV2_DIM3) + col*2*(CONV2_DIM3) + depth; //00
        e2 = row*2*(CONV2_DIM2)*(CONV2_DIM3) + (col*2 + 1)*(CONV2_DIM3) + depth;//01
        e3 = (row*2 + 1)*(CONV2_DIM2)*(CONV2_DIM3) + col*2*(CONV2_DIM3) + depth; //10
        e4 = (row*2 + 1)*(CONV2_DIM2)*(CONV2_DIM3) + (col*2 + 1)*(CONV2_DIM3) + depth;//11
        op_offset = row*(MAXPOOL2_DIM2)*(MAXPOOL2_DIM3) + col*(MAXPOOL2_DIM3) + depth;
        output[op_offset] = max4(input[e1],input[e2],input[e3],input[e4]);
        }
        }
    }
Observation : A53 and x86 use Vector and SIMD instructions respectively
 with Compiler Optimization (-O3)

---
Matrix Vector Multiplication [1 x 300] x [300 x 300]
  3 void vmatmul(float vect[], float mat[],int vdim, int mat_dim2, float res[])
  4 {
  5 // Multiply [ 1 x dim1] x [dim1 x dim2]
  6 int mat_offset;
  7 float mac;
  8 float prod, mult_1, mult_2;
  9 for (int i=0;i<mat_dim2;i++)
 10 {
 11 mac=0;
 12 for(int j=0;j<vdim;j++)
 13 {
 14 mac += vect[j] * (*(mat + mat_dim2*i + j));
 15 }
 16 *(res+i) = mac; //store result into product
 17 }
 18 }

---
Cache Memory Profiling
Cache Level-wise Profile	x86	Cortex-A53	X86 with -O3	A53 with -03
I refs	193 809 805	192 768 160	25 663 967	25 987 578
I1 misses	882	1139	879	1 121
LLi Misses	877	832	875	812
D refs	82 153 327	86 582 493	7 705 355	7 872 700
D1 misses	3 350 271 (4.1 %)	3 354 623 (3.8 %)	3 355 431 (43.5%)	3 355 668(42.6 %)
LLd misses	7 320	7122	8197	7 086
Inference: Results are similar and cache memory performance is sufficiently good for Convolution

---
Week 6
- Week 5 :Action
- Run Neon Assembly for understaind its performance better
- Agenda
- Survey of ARM based Vector Extensions
- Study of ARM’s Edge ML Inference SoC

---
ARM SIMD ISAs
https://developer.arm.com/architectures/instruction-sets/simd-isas

---
Scalable Vector Extension (SVE)
- SVE enables vectorization of loops which would either be impossible or not beneficial to vectorize with Neon.
- Scalable Vector Length
- Vector code allows each implementation to automatically choose its vector length, provided it is a multiple of 128 bits and does not exceed the architectural maximum of 2048 bits. SVE provides 32 scalable vector registers, named Z0 – Z31.
- Per-lane predication
- SVE provides 16 predicate registers, named p0-p15, with each predicate register being 1/8th of the size of the vector register (1 bit per byte), and therefore scalable in size. Predicate registers are written to use condition-creating instructions, such as compares. Condition-creating instructions allow later instructions to control which elements (or 'lanes') that a vector should be operated on (the 'active' elements).
- Gather-load and scatter-store
- Gather-load and scatter-store allows data to be efficiently transferred to or from a vector of non-contiguous memory addresses. The efficient transfer of data enables a wider range of source code constructs to be vectorized. To permit efficient accesses to contiguous memory, SVE provides an extensive set of load and store instructions which progress sequentially forwards through an array, supporting a full range of packed 8, 16, 32, and 64-bit vector element organizations.

---
Neon ARM Vector Floating Point Processor
- SIMD architecture extension for the Arm Cortex-A and Cortex-R series processors.
- Neon technology is a packed SIMD architecture.
- Neon registers are considered as vectors of elements of the same data type, with Neon instructions operating on multiple elements simultaneously.
- Adds about 23 new instructions
https://developer.arm.com/architectures/instruction-sets/simd-isas/neon

---
Packed SIMD Data Processing
- Seperate Vector Register File that features 128 bit data.
- Perform the same operation simultaneously for multiple data items. These data items are packed as separate lanes in a larger register.
- The diagram shows 128-bit registers each holding four 32-bit values, but other combinations are possible for Neon registers:
1. Two 64-bit, four 32-bit, eight 16-bit, or sixteen 8-bit integer data elements can be operated on simultaneously using all 128 bits of a Neon register.
2. Two 32-bit, four 16-bit, or eight 8-bit integer data elements can be operated on simultaneously using the lower 64 bits of a Neon register (in this case, the upper 64 bits of the Neon register are unused).
https://developer.arm.com/architectures/instruction-sets/simd-isas/neon/neon-programmers-guide-for-armv8-a/introducing-neon-for-armv8-a/data-processing-methodologies

---
Classes of Instructions
1. Load /Store : vldr/vstr, vldm, vstm
2: Data Processing: vadd, vsub, vmul, vnmul, vdiv
3. Data Movement vmov,
4. Data type Conversion vcvt
Packed SIMD Drawbacks :
1. The length of all vectors is clamped
2. All operands should be of same type.

---
Helium ISA Extension
- Helium is a new ground-up design that enables efficient signal processing performance in small processors. It provides many new architectural features that are not available in Neon. The key differences between Helium and Neon are as follows:
- Helium is optimised for low power, high performing CPUs. As such, the architecture is designed to maximise usage of all available hardware.
- Helium has fewer vector registers than Neon, however, some Helium vector instructions can access the scalar register file and the vector register file simultaneously.
- Helium  supports features like loop predication, lane predication, complex maths operations, and scatter-gather memory accesses.
- Vector Processing Support
- 2 x 32-bit MAC/cycle
- 4 x 16-bit MAC/cycle
- 8 x 8-bit MAC/cycle

---
ARM Ethos-U55 NPU for ML
- Coprocessor for ARM-Cortex M55
- Embedded ML Inference on Cortex-M uCs
- Designed to accelerate ML inference in area-constrained embedded and IoT devices.
- Uses: ARM Helium Vector ISA extension
- Helium is analogous to NEON for ARM-CortexM Series

---
ARM Ethos-U55 NPU for ML – introduced in Feb 2020
https://www.brighttalk.com/webcast/17792/391867/technical-overview-of-the-arm-cortex-m55-and-ethos-u55-processors

---
Features
- > 150 new scalar and vector instructions
- Low overhead loops (due to predication)
- Weight Decoder and DMA for on the fly weight decompression (Weight Compression done offline)
- Configurable MAC(32/64/128/256)
- Ethos-U55 can completely execute networks that map to the supported operator set. Such as : Deepspeech-V1 , RNNNoise, Wav2letter ,
- Any unsupported operation falls back to Cortex-M55 for execution
- Softmax is not supported
Execution Flow

---
https://www.brighttalk.com/webcast/17792/391867/technical-overview-of-the-arm-cortex-m55-and-ethos-u55-processors

---
Week-7 and 8
- Getting Started with ARM Assembly
- Disassembly analysis of Arm Neon Code using Raspberry Pi 3
Assemling on ARM
as -g main.s -o main.o
as -g mvmul.s -o mvmul.o
ld -o mvmul main.o mvmul.o

---
Fact Check
	Understanding	Source
1.	Raspberry Pi3 contains ARM Cortex A53	Rpi3 User manual
2.	Raspberry Pi3 contains ARM Neon CoProcessor	Cortex A53 Datasheet
3.	Command for Compiling NEON Assembly on Rpi is: / gcc -mfpu=neon-vfpv4 -o <exe> <src1.c> <src2.c> ...	1. ARM v8 Programmers Manual, / 2. Raspberry Pi Assembly Language Programming by Stephen Smith (z-lib.org) / 3. If Flag not given, “illegal instruction” compiler error pops up.

---
Programming with NEON
- SIMD Topology
- Can operate on 8,16,32 bit INT and Single Precision Float Numbers.
- It cannot perform 64-bit or 128-bit arithmetic.
- All elements getting operated should be of the same type.
- Greatest Parallelism is obtained using INT8.

---
Lanes
Depending on the data-type, the NEON divides the 128-bit register into equal lanes of size (128/size_of_datatype)

---
Example: Distance in 4D
gcc -mfpu=neon-vfpv4 -o distance distance.s main.s
Generates Executable on NEON. If the -mfpu is not specifed, illegal instruction error is obtained during compilation. Source : https://gcc.gnu.org/onlinedocs/gcc/ARM-Options.html

---
SIMD Coding for Matrix Vector Multiplication on NEON : Matrix 3x3 Vec 3x1
- Put a, d, and g in a register in separate lanes
- b, e, and h in another register in matching lanes
- c, f, and i in a third register in the matching lanes
- Multiply each of the lanes with x,y and z respectively and then add all three vector
- Thus, there are no loops
- All three coumns of the output are computed parallely

---
NEON Assembly vs NEON C Code
- C Code for Matrix Vector Multiplication compiled for NEON does not use the optimal SIMD discussed in the previous slide.
- Instead, it continues to loop three times for a 3x3 Matrix .
- Inference : gcc for NEON does not auto-vectorize

---
SIMD Assembly for NEON
- Hand-coded Assembly Program for Matrix Vector Multiplication using SIMD programming
- Steps are:
- 1. Load 3x3 Matrix A into Q0, Q1 and Q2
- 2. Load 3x1 Vector X into Q3.
- 3. Multiply each of Q0, Q1, Q2 with Q3
- 4. Perform Pair-wise addition of elements inside the products
- 5. Store Results in Y (3 x 1)

---
Disassembly of NEON Assembly Code for VMATMUL

---
VMATMUL for C Code targetting NEON

---
Observations
1. Even with -O3 optiization, the code does not produce SIMD Code for Matrix Vector Multiplication of size 3x3.
2. NEON SIMD is not scalable for Matrices beyond 4 rows as the intermediate results have to be stored onto Stack and then retrived.

---
Desirable Instructions
1. Dot product of two Vectors : Exists in NEON but is only supported for INT8 numbers
2. Add all elements in a vector register (currently, only Pair Add is available)