RISC-V for AI
Literature Survey and Profiling Analysis

---
Analysis of CNNs
1. CNN for MNIST dataset :
2. Neural Network Architecture
12. Coded the network in C and executed on x86 and riscv platforms and results were verified.
Layer (type) Output Shape Param #
=================================================================
conv2d (Conv2D) (None, 24, 24, 32) 832
_________________________________________________________________
max_pooling2d (MaxPooling2D) (None, 12, 12, 32) 0
_________________________________________________________________
conv2d_1 (Conv2D) (None, 8, 8, 64) 51264
_________________________________________________________________
max_pooling2d_1 (MaxPooling2 (None, 4, 4, 64) 0
_________________________________________________________________
flatten (Flatten) (None, 1024) 0
_________________________________________________________________
dense (Dense) (None, 10) 10250
=================================================================
Total params: 62,346
Trainable params: 62,346
Non-trainable params: 0
_________________________________________________________________

---
Profiling Analysis of CNN
1. Done using Valgrind and Kcachegrind tools

---
Convolution -only Profiling
1. Done using Valgrind and Kcachegrind tools
2. 1. Work-load division

---
Analysis
1. 1. Computing Array Indicies consume considerable amount of time(about 33%)
2. Formula: x1*d2*d3*d4 + x2*d3*d4 + x3*d4 + x4
3. Idea: For upto 4D arrays, whose dimension along each axis is < 256, the index computation can be vectorized.
4. Algorithm for Accelerating the above computation
5. We store these in 2 registers say, r1,r2 as 8-bit unsigned integers:
t	r1	r2	r3	r4	r5
0	x1,x2,x3,x4	d1,d2,d3,d4
1			x1*d2, / d3*d4		x3*d4
2				r3[31:16]+x2	r5+x4
3				r3+r4
4					r4+r5
r1	x1	x2	x3	x4
r2	d2	d3	d4
Using 8 bit Multipler with
 4 clock cycles
(CSA+Wallace Tree),
 this operation can be
completed within 10 clocks

---
High Level Synthesis of Offset Compute
Hardware accepts 2 int arrays , x and d as inputs and returns an integer
It extracts x1,x2,x3 andx4 ; d2,d3,d4 using AND and Shift Ops and passes it to
offset_compute

---
Desirable elements in an low-power RISC processor for ML
1. 1. ISA Extensions for commonly used instructions such as vector/tensor operations
2. 2. Scratch-pad memory for working with intermediate results
3. 3. Resource efficient Floating Point Unit – bfloat16, DLFLoat

---
Brain Floating Point - bfloat16
1. 16-bit FPU alternative to IEEE754 Half Precision FPU
2. Format : 1(sign) + 8(exp) + 7(mantissa).
3. Used in Google TPU cloud v3 MAC units. Multiplication is done in bfloat16 while Accumulation is done in FP32.
4. AMD likely to incorporate
6. DL Float16- Floating Point format for DL Training and Inference
7. 1. Format : 1(sign) + 6(exp) + 9(mantissa)
8. 2. FMA Hardware : Fused Multiply Add

---
Fused Multiply Add Hardware
1. Useful for Matrix Multiplications, Convolutions
2. R = C + A*B
4. FMA in blfloat is mixed(blfloat-16 for multiplications and FP-32 for add). However, in DLFloat FMAs, it is fully DLFloat-16

---
DSP ISA augmentation to RISC-V
Paper on PULP-RISCV core for IoT
1. Microarchitectural Improvements to RISCV32IM
2. 1. 4-core with shared TCDMs
3. 2. Instruction Pre-fetch buffer + Shared I-Cache
4. 3. ALU Datapath enables operations on 8-bit / 16-bit vectors, supporting unaligned memory accesses.
5. 4. Instructions for Packed-SIMD,Fixed-point , shuffling bytes in a word and hardware loop unrolling, dot-product

---
Algorithms for Accelerating Activations
CORDIC : To study

---
Week-3 (Aug 7-14, 2020)
1. Week 2 Actions
2. 1. Perform profiling of various other ML algorithms and other Neural Network Topologies and find out if there can be any general instructions for spped up.
3. 2. Exploration of Implementing Brain Float 16 FPU to be explored.

---
Week -3 :Profiling Other ML Algorithms
1. 1. Unsupervised Learning – Principle Component Analysis (PCA)
2. Use Case: To reduce the Size of Input Dimensions for classifying MNIST Dataset
3. A 4-layer fully-connected Neural Network is used for MNIST digit classification where the input dimension is 784.(28x28)
11. Since Image matrices are sparse, their variances will be limited to only a subset of 784 dimensions. PCA is used to capture the most significant Eigen Vectors in the Image Dataset (60,000 x 784).
12. The plot aside shows the fraction of variance of the Image Dataset that can be catured as a function of the number of significant eigen vectors used. So, in order to capture 75% of the variance in the images, only 100 out of 784 dimensions are sufficient.

---
PCA-Inference
1. The Neural Network Model for the reduced set of Inputs (100) is shown below:
2. It can be seen that the new model
3. features only ~4,000 parameters as
4. Compared to ~26000 in the original one
6. Computational Overhead
7. In the inference engine,
8. 1. All inputs have to be normallized to Zero-mean and UNIT standard deviation.
10. 2. These scaled inputs(784 dim) have to be transformed to 100-dimension space using SVD matrix. This results in a matrix – vector multiplication
11. INPUT_TRANSFORMED = [ 1 x 784 ] * [784 x 100] with 78400 multiplications.
12. The PCA-transformation + 4 layer NN was coded in C language and profiled with Valgrind.
13. Result : 85% of the processor cycles are used for PCA.(3 442 401 cycles ) (115 648 537 cycles for Conv2D)
14. Followed by 3% load (117 266) cycles for perceptron
15. Followed by 1.25% for 47 136 cycles for normallizing function.

---
Autoencoder
1. Studied Auto-encoder
2. Use Case: Same as PCA
3. Auto-encoders can be designed using the same structre as used for PCA.
4. Auto-encoders and PCA differ in the way they are trained.
5. Thus, computational load is expected to be the same.

---
Week 4:
1. Week3 Actions:
2. 1. Cambricon is a useful paper. Get statistics on computational load of instructions used in Deep Learning operations from the paper.
  2. Continue profiling for other NN topologies.
3. ----------------------
4. Week 4:
5. Realized mistakes in coding styles
6. 1. Use of malloc() to be avioded as it consumes substantial amount of time itself. Instead crete all arrays and allocate memory for them during compile time. Tradeoff: Generallization
7. 2. Rmove all funtion calls inside forloops . They add to enormous amounts of push-pop overheads.

---
Week-4 : Recurrent Neural Network
2. RNN for classifying Sequential MNIST dataset.
4. Each image is fed to the RNN one row at a time.
5. Input Dimensions = 28
6. LSTM-1 Layer has 128 neurons
7. LSTM-2 layer has 128 neurons
8. The output of the last LSTM layer (128 dimensions) is fed to 3-layer perceptron to obtain class conditional densities 0->9.
Layer (type) Output Shape Param #
=================================================================
lstm (LSTM) (None, 28, 128) 80384
_________________________________________________________________
lstm_1 (LSTM) (None, 128) 131584
_________________________________________________________________
dense (Dense) (None, 64) 8256
_________________________________________________________________
dense_1 (Dense) (None, 10) 650
=================================================================
Total params: 220,874
Trainable params: 220,874
Non-trainable params: 0

---
LSTM
Source: https://medium.com/analytics-vidhya/demystifying-lstm-weights-and-biases-dimensions-c47dbd39b30a

---
Implementation and Profiling Results
C-code compiled and run on x86. For infering 1 image, the following are the profiling results:-
1. Profiling Results show that RNN takes a total of 148,051,630 cycles to complete one run, almost thrice as long as CNN (830 648 537)
Mthematical Operation	%Exe. Time / Of the total prgm	No. of times called	Avg Execution cycles per call
Matrix Vector Multiplication / [1 x 128]* [128 x 128] / [1 x 28] * [28 x 128] / [1 x 128] * [128 x 64] / [1 x 64] * [64 x 10]	96.92%	450	409, 245 / 251, 335 / 40, 680
2 vector Addition (128)	1.04%	506	~3,000
exponent(x)	0.72%	35, 904	30

---
Profiling Matrix Vector Multiply
1. 1. In order to obtain percentage of time a given piece of code took for execution, a function was created. This function was being called from the program.Problem: Since the funtion is repeatedly called from inner loop, execution overheads suck as stack operations were found to each away a significant amount of time. (almost 50% of original function time)
2. 2. Therefore, all functions called within loops were removed; Code was flattened.
3. Line-wise Assembly Level Code breakup for Matrix vector Multiply
4. Total Assembly Instructions(x86): 65
5. Innermost loop	: 24 instructions
6. Break up:
7. Offset Calculation : 6
8. Load ith element : 7
9. Load ijth element : 8
10. Multiply : 3
11. Accumulate : 3

---
Ara: RISC-V Vector Processor, Oct 2019, arXiv
1. Specifications:
2. 64-bit Vector processor based RISC-V’s vector extension ISA
  Freq of Operation ~ 1.2 GHz
3. Performance : 33 Dp-GFLOPS (41 DP-GFLOPS/Watt)
4. Power : 794 mW (max.)
6. Main Idea: Exploits regularity in Parallel Data Workloads
7. Vector Instruction: A single vector instruction can be used to express a data-parallel computation on a very large vector => Reduces Fetch, Decode , Store Overhead significantly.
8. Advantage over GPUs
9. In Single Instruction- Multiple thread(SIMT) architectures, the fetch.decode,store overhead amortization is limited to the number of execution elements in a proessing block (32, 64). Whereas, in Vector Processors, there is no cap on Vector length.

---
Architectures to handle Vector data
1. Array Processors: Implement Packed-SIMD architecture
- Several independent processing elements having a
- Common control unit
- Limitation : Vector length is fixed.
- Ex: Intel Streaming SIMD Extension (SSEs), ARM Neon,
  RISC-V DSP extension
2. 2. Vector Processors
3. Time-multiplexed version of Array Processors, implemening
4. vector-SIMD instructions
5. Several speciallized functional units stream the
6. micro-operations on consecutive cycles, as shown in figure.
7. By doing so, the number of functional units no longer
8. constrains the vector length.
9. Ex: Cray SuperComputer, ARM Scalable Vector Extnsion,
10. Fujitsu A64FX

---
Microarchitecture
1. Ara works in tandem with Ariane, an open source Linux Capable application-class core
2. Ariane has been been extended to drive the accompanying vector unit as a tightly coupled
3. co-processor
4. Ariane:
5. Six-Stage Pipeline
6. In-order
7. All vector instructions are decoded in Ara.
8. Handshaking mechanism between Ara and Ariane
10. Consists of Several lanes.
11. Each lane can handle Upto 8 instructions in Parallel

---
Results
1. Benchmarking:
2. Y <-- aX + Y =>Memory Intensive
3. Convolution =>Compute Intensive
4. Matrix Multiplication : Moderately Computationally Intensive
5. Performance figures:
6. No comparison done with a non-vector processor

---
Performance with Different Lane Widths

---
Vector Architectures contd ...
1. 3. SIMT : Single instruction to multiple independent threads running in parallel
2. Ex: NVIDIA Volta GPU
3. While this model is efficient to handle data intensive workloads, it consumes substantial power
5. 4. Vector Thread: A compromise between SIMD and MIMD.
6. Supports Loops with cross iteration dependencies
7. Main difference between SIMT and VT is that in the latter the vector instructions reside in another thread, and scalar book-keeping instructions can potentially run concurrently with scalar ones.
8. This division alleviates the problem of SIMT threads running reduendant scalar instructions that must be later coalesced in hardware

---
Lane Microarchitecture
1. Each lane has :
2. 1. Lane Sequencer that can keep track of upto 8 parallel instructions
3. 2. Vector RegFile(which can be accessed by other lanes as well), Operand Queues
4. 3. Integer ALU, Integer MUL, FPU

---
Paper Summary: “Cambricon : AN ISA for Neural Networks” ACM/IEEE-2016
1. Propose a domain specific Instruction Set Architecture for NN Accelerators
2. Integrates Scalar, Vector, Matrix,logical, data transfer, and control instructions based on a comprehensive analysis of existing Neural Network Techniques
3. Architecture Highlights:
4. 1. Accelerator is designed to accept instruction sequentially and run like a processor.
5. 2. Data-level parallelism :- Instructions to load Vectors and matrices onto scratch-pad memory from Main Memory
6. 3. Scratch Pad Memory :- Uses Scratch Pad memory(High speed) for fast computations instead of the Register Files and Cache Memories.
7. 4. Vector /Matrix Instructions :- Dot-product, ADD, SUB, MULT for matrix and vectors
8. 5. Engines for computing vector-wise (exp(x), log(x), tanh(x)) using CORDIC algorithm
10. Evalutation:
11. Evaulated over ten representative NN techniques:- MLP, CNN, RNN, LSTM, Autoencoder, Sparse Autoencoder, Boltzmann machine, RBM, Self Organized Mapping and Hopfeld NN.

---
Microarchitecture

---
Cambricon Performance Results